AUDIBLE AND VISIBLE HIGH-WAY CROSSING SIGNAL

Taken from:

The Signal Engineer, October, 1914

Simplicity of operation was the goal, which was aimed at in the development of the Automatic

Flagman and Crossing Bell, illustrated below.  This device, which. is being placed on the

market by the Railway Specialties Company of Los Angeles, Cal., operates without motor or

solenoid, the operating mechanism consisting of two Electro-magnets and a switch for turning

IC current alternately from one Electro-magnet to the other. The red disk swings through an

angle of approximately 72 degrees at the rate of 60 strokes a minute, 30 strokes each way. At

the same time, the red light is turned on.

The two operating magnets may be designed for either direct or alternating current.  For use

on steam railways the prevailing type is wound for 8 volts, d. c.  For electric railways, the

windings range from 500 to 1,200 volts, d. c., and for a. c. current the windings are for 110 or

220 volt, a. c.

There are but two bearings in the entire apparatus.  The bearings supporting and operating the

swinging target are 1 3/8 in. long and are made of babbitt.  The walking-beam is separately

pivoted and has ball bearings.  The armature is swung below the main  bearing between the

two Electro-magnets. When the current is cut in, the armature is pulled toward the energized

magnet and this operation mechanically throws the walking-beam switch to the opposing

magnet.  As the armature gets near the energized magnet, an independent circuit is cut which

lights the bullseye a simple mechanical attachment to the rocker-shaft actuates the gong.

For starting or stopping the signal, either the open or closed system may be employed, the

closed circuit being commonly used on steam railroads in connection with an interlocking

relay in the same manner as for operating the block signals.  For electric railway operation, the

open circuit is employed, a contactor being placed on the trolley or third rail at the desired

distance.  This diverts current to a high-voltage relay, which is furnished as a part of the

crossing-signal apparatus.  A similar contactor at the crossing disconnects the circuit as the

train passes.

The illustration shows the simplicity of the machinery necessary for operating the signal.  The

old crossing bell and telegraph pole have since been removed.

Taken from:

The Signal Engineer, October, 1914

Thanks to Per Olofsson for sending this in.